TIMER CIRCUITS

The 555 Timer

The 555 timer is a versatile and widely used device because it can be configured in two different modes either as a monostable multivibrator (one-shot) or as an astable multivibrator (oscillator). An astable multivibrator has no stable states and therefore changes back and forth (oscillates) between two unstable states without any external triggering.

Basic Operation

A functional diagram showing the internal components of a 555 timer is given in Fig. (1).

The comparators are device whose outputs are HIGH when the voltage on the positive (+) input is greater than the voltage on the negative (-) input and LOW when the (-) input voltage is greater than the (+) input voltage. The voltage divider consisting of three (5-k) resistors provides a trigger level of and a threshold level of . The control voltage input (pin 5) can be used to externally adjust the trigger and threshold levels to other values if necessary. When the normally HIGH trigger input momentarily goes below, the output of comparator B switches from LOW to HIGH and set the S-R latch, causing the output (pin 3) to go HIGH and turning the discharge transistor Q1 off. The output will stay HIGH until the normally LOW threshold input goes above and causes the output of comparator A to switch from LOW to HIGH. This resets the latch, causing the output to go back LOW and turning the discharge transistor on. The external reset input can be used to reset the latch independent of the threshold circuit. The trigger and threshold input (pin 2 and 6) are controlled by external components connected to produce either monostable or astable action.

Monostable (One-Shot) Operation

An external resistor and capacitor connected as shown in Fig. (2) are used to set up the 555 timer as a non-retriggerable one-shot. The pulse width of the output is determined by the timer constant of R1 and C1 according to the following formula:

tW =1.1 R1.C1.                                                                                            (1)

the control voltage input is not used and is connected to a decoupling capacitor C2 to prevent noise from affecting the trigger and threshold levels.

Before a trigger pulse is applied, the output is LOW and the discharge transistor Q1 is on, keeping C1 discharge as shown in Fig. (3a). When a negative-going trigger pulse is applied, the output goes HIGH and the discharge transistor turns off, allowing capacitor C1 to begin charging through R1 as shown in Fig. (3b). When C1 charges to , the output goes back LOW and Q1 turn on immediately, discharging C1 as shown in Fig. (3c). As you can see, the charging rate of C1 determines how long the output is HIGH.

EXAMPLE.1

What is the output pulse width for a 555 monostable circuit with R1=2.2 k and C1=0.01 F?

Solution

From equation (1) the pulse width is

tw=1.1 R1.C1=1.1*(2.2 kFs.

Homework

For C1=0.01F, determine the value of R1 for a pulse width of 1 ms.

Astable Operation

A 555 timer connected to operate as an astable multivibrator, which is      a non-sinusoidal oscillator, is shown in Fig. (4). Notice that the threshold input (THRESH) is now connected to the trigger input (TRIG). The external components R1, R2, and C1 from the timing network that sets the frequency of oscillation. The (0.01 F) capacitor C2 connected to the control (CONT) input is strictly for decoupling and has no effect on the operation in some cases it can be left off.

Initially, when the power is turned on, the capacitor (C1) is uncharged and thus the trigger voltage (pin 2) is at (0 V). This causes the output of comparator B to be HIGH and the output of comparator A to be LOW, forcing the output of the latch, and thus the base of Q1, LOW and keeping the transistor off. Now, C1 begins charging through R1 and R2 as indicated in Fig. (5). When the capacitor voltage reaches, comparator B switches to its LOW output state, and when the capacitor voltage reaches, comparator A switches to its HIGH output state. This resets the latch, causing the base of Q1 to go HIGH and turning on the transistor. This sequence creates a discharge path for the capacitor through R2 and the transistor, as indicated. The capacitor now begins to discharge, causing comparator A to go LOW. At the point where the capacitor discharges down to, comparator B switches HIGH; this sets latch, making the base of Q1 LOW and turning off the transistor. Another charging cycle begins, and the entire process repeats. The result is a rectangular wave output whose duty cycle depends on the values of R1 and R2. The frequency of oscillation is given by the formula

(2)

By selecting R1 and R2, the duty cycle of the output can be adjusted. Since C1 charges through R1+R2 and discharges only through R2, duty cycles approaching a minimum of 50 percent can be achieved if R2>>R1 so that the charging and discharging times are approximately equal.

An expression for the duty cycle is developed as follows. The time that the output is HIGH (tH) is how long it takes C1 to charge from to. It is expressed as

(3)

The time that the output is LOW (tL) is how long it takes C1 to discharge from to . It is expressed as

(4)

The period, T, of the output waveform is the sum of tH and tL.

(5)

This is the reciprocal of (f) in equation (2). Finally, the duty cycle is

(6)

To achieved duty cycles of less than 50 percent, the circuit in Fig. (4) can be modified so that C1 charges through only R1 and discharges through R2. This is achieved with a diode D1 placed as shown in Fig. (6). The duty cycle can be made less than 50 percent by making R1 less than R2. Under this expression for the duty cycle is

EXAMPLE.2

A 555 timer configured to run in the astable mode (oscillator) is shown in figure below. Determine the frequency of the output and the duty cycle.

Solution

Use Equations (2 and 6).

Homework

Determine the duty cycle in figure above if a diode is connected across R2 as indicated in Fig. (6).

# Text boxes

Fig. (1): Internal functional diagram of a 555 timer

(Pin numbers are in parentheses).

_

_

+

+

The 555 Timer

(3)

(5)

(6)

(2)

(7)

(1)

(4)

(8)

R

5k

R

5k

R

5k

S

R

Q

Q1

Discharge transistor

Comparator B

Comparator A

Latch

Output buffer

Output

Reset

GND

VCC

Discharge

Trigger

Control voltage

Threshold

TRIG

THRESH

DISCH

RESET

VCC

CONT

OUT

The

555

Timer

(8)

(5)

(3)

C2

GND

(1)

(2)

(6)

0.01 F

(decoupling optional)

C1

R1

(7)

(4)

+VCC

Fig. (2): The 555 timer connected as a one-shot.

0 V

C1

R1

B

A

_

_

+

+

The 555 Timer

(3)

(5)

(6)

(2)

(7)

(1)

(4)

(8)

R

5k

R

5k

R

5k

S

R

Q

Q1

ON

LOW

LOW

HIGH

LOW

Output

VCC

HIGH

Trigger

Fig. (3a): Prior for triggering.

t0

0

VC1

t0

Charging

C1

R1

B

A

_

_

+

+

The 555 Timer

(3)

(5)

(6)

(2)

(7)

(1)

(4)

(8)

R

5k

R

5k

R

5k

S

R

Q

Q1

OFF

LOW

t0

Output

VCC

Fig. (3b): When triggered.

1.1R1C1

t1

t1

HIGH

t1

2/3VCC

t0

0

VC1

Discharging

at t1

C1

R1

B

A

_

_

+

+

The 555 Timer

(3)

(5)

(6)

(2)

(7)

(1)

(4)

(8)

R

5k

R

5k

R

5k

S

R

Q

Q1

ON

LOW

Output

VCC

Fig. (3c): At end of charging interval.

R2

TRIG

THRESH

DISCH

RESET

VCC

CONT

OUT

The

555

Timer

(8)

(5)

(3)

C2

GND

(1)

(2)

(6)

0.01 F

(decoupling optional)

C1

R1

(7)

(4)

+VCC

Fig. (4): The 555 timer connected as an astable multivibrator (oscillator).

t0

t1

t0

Charging

_

+

R2

+VCC

1

1

2

2

1

1

2

2

Vout

On

Off

On

Discharging

C1

R1

B

A

_

_

+

+

The 555 Timer

(3)

(5)

(6)

(2)

(7)

(1)

(4)

(8)

R

5k

R

5k

R

5k

S

R

Q

Q1

+VCC

1

1

2

2

2

1/3VCC

2/3VCC

Fig. (5): Operation of 555 timer in the astable mode.

_

+

D1

R2

TRIG

THRESH

DISCH

RESET

VCC

CONT

OUT

The

555

Timer

(8)

(5)

(3)

C2

GND

(1)

(2)

(6)

0.01 F

C1

R1

(7)

(4)

+VCC

Fig. (6): The addition of diode D1 allows the duty cycle of the output to be adjusted to less than 50 percent by making R1<R2.

R2

4.7k

TRIG

THRESH

DISCH

RESET

VCC

CONT

OUT

The

555

Timer

(8)

(5)

(3)

C2

GND

(1)

(2)

(6)

0.01 F

C1

0.022 F

R1

2.2k

(7)

(4)

+5.5 V