Turn-on Dynamic of Field and Photon-Assisted Polarization in InGaAs/GaAs QD Laser with wavelength of 1.3 μm

R. M. Hassan, C. A. Emshary and S. I. Easa

Dept. of Physics, College of Education, University of Basrah. Basrah, IRAQ

Abstract

With using master equations model of quantum dots (QDs) laser theory by C. Gies and his colleagues (2007), we have added a new factor to the s-shell population’s equations to take into account the retardation procedure in the turn-on dynamics. The addition has led to theoretical results nearly in isomorphism with experimental data. We are presented a theoretical simulation of the turn-on dynamics of InGaAs/GaAs semiconductor QD laser output lasing with CW wavelength of 1.3μm at room-temperature including the photon-assisted polarization contribution.

الخلاصة

من خلال أستخدام نموذج المعلدلات الرئيسية لنظرية ليزر النقاط الكمية  (QDs) لكرستفل هيل و مشاركيه (2007) , أضفنا معامل جديد الى معادلات تعداد طبقة-s للأخذ بنظر الاعتبار أجراء التأخير في حركيات بدء التشغيل. تؤدي هده الأضافة الى نتائج نظرية مقاربة للبيانات العملية. قدمنا محاكات نظرية لحركيات بدء التشغيل في ليزر النقطة الكمية نوع  InGaAs/GaAs بطول موجي 1.3 μm عند درجة حرارة الغرفة تتضمن أسهام الأستقطاب المصاحب للفوتون.

Introduction

Consider lens-shaped InGaAs/GaAs QDs grown in the Stranski-Krastanow growth mode [Peter Michler (2003), Todd Steiner (2004), Chun-Hua Yuana, et. al. (2006), and Swati Ramanathan (2007)]. In this process a thin film of a few nanometer thicknesses called wetting layer (WL) is formed between the QDs and the substrate. The QDs and the WL constitute a coupled system with common electronic states. Typical dimensions of the QDs are 25nm base diameter and less than10nm in height [Martin J. Stevens, et. al. (2006)]. The geometry of this kind of QDs allows for a description within the effective mass approximation, where free carrier dispersion with effective masses for electrons and holes is assumed. One can consider the first two confined shells of such a system, which are denoted by s and p according to their in-plane symmetry. The s-shell is only spin degenerate, while the p-shell has additional angular- momentum two-fold degeneracy [T. R. Nielsen, et. al. (2004)].The spectrum of the potential well introduces a splitting into sub bands with a spacing that depends on the strength of the axial confinement, although the term sub band is somewhat misleading for the QD case, as these possess only a discrete spectrum due to the additional in-plane confinement [T. Feldtmann, et. al. (2006)].

The discrete states are located energetically below a quasi –continuum of delocalized states, corresponding to the two-dimensional motion of carries in a WL. While, the localized states exist only below the quasi-continuum states of the WL [Emmanuel Rosencher , et. al. (2004), M. Lorke, T. R. Nielsen, et. al. (2006), and Voicu Popescu, et. al. (2009)]. In Fig.1, a schematic diagram of the energy levels of the coupled QD−WL system is shown. Further details of the QD model are discussed in Ref.[ T. R. Nielsen, et. al. (2004)]. Strictly speaking, the localized states and the WL states are solutions of the single-particle problem for one common confinement potential and must, therefore, form an orthogonal basis [Peter Michler (2003), Todd Steiner (2004), T. R. Nielsen, et. al. (2004), and  Paul Harrison (2005)]. In this work, we focus on modulation of the laser theory model for semiconductor QDs in microcavities in Refs.[ N. Baer, et. al. (2006) and Christopher Gies, et. al. (2007)], which express a site of master equations of semiconductor QDs lasers.

Figure 1: Schematic of the coupled QD-WL system.

Theory

When one use the theoretical model of laser theory for semiconductor QDs in microcavities [N. Baer, et. al. (2006) and Christopher Gies, et. al. (2007)] to study the turn-on dynamics and relaxation oscillations in the InGaAs /GaAs QD laser with a wavelength of 1.3 µm one get a poor agreement with experimental results, i.e. the theory is not accurate enough and not able to interpret the produced work by other researchers [Marius Grundmann (2000), M Grundmann (2000), and Matthias Kuntz]. Since they did not take into account the delay time inherent to occur between pumping process and building the enough population inversion, which leads to the gain then the production of electromagnetic field. To overcome this problem, we have added a factor to the s-shall populations equations to take into account the retardation procedure. This addition has led to theoretical results nearly in isomorphism with experimental data in comparison to what can be gained from Ref.[Christopher Gies, et. al. (2007)].

The correlation functions have the following expressions [Christopher Gies, et. al. (2007)]:

The first term in this equations describes the carrier dynamics due to the interaction with the laser mode, which has the main effect of this poor agreement. We can assume here a factor   is one of the structure parameters that is a ratio of the doping barriers in quantum dots, where   is the value of n-doped (p-doped) barrier density respectively. The new addition  ) is called a Dynamical Delay Factor (DDF) which is vary in region   due to the depend barrier in quantum dots materials is p- type ( around 1017 cm-3 [Matthias Kuntz (2006) and Ryan R. Alexander, et. al. (2007)]). That is normalize the model to make a good agreement with experimental results [Marius Grundmann (2000)] when one studies the turn-on dynamics semiconductor QD lasers..

We present the QD laser master equations model (MEM), which is instructive here to study relaxation oscillations in semiconductor QD Lasers. The Photon-Assisted Polarization (PAP) from this model ignoring spontaneous emission for the above - threshold solution, and expressing the higher-order correlations. For this purpose, we use the stationary limit of MEM, we can write:

where    is electron / hole population of s-shell (p-shell),  is the pump rate,  is s-shell (p-shell) spontaneous emission rate into non-lasing modes,  is electron / hole spontaneous emission rate into lasing modes, k the total cavity loss,  is a dephasing of phenomenological,  is the Photon-Assisted Polarization (PAP), and  is the spontaneous emission coupling factor.

In the following we shall use the site of QD semiconductor laser MEM (1)-(4) to compute numerically to study the turn-on dynamic of field with contribution of photon-assisted polarization in InGaAs /GaAs QD Lasers.

The ordinary differential system MEM (1)−(4) includes the time variation of photon population  in the QD laser cavity,   photon-assisted  polarization      s-shall ∕ p-shall carriers populations of electron and hole ( and  respectively). These variables are functions to various parameters (i.e. control parameters). Table (1) constitutes these parameters with their values and units which are used in the present work. The pump rate is one of the important time dependent parameter.

Calculations and results

To control the dynamical interaction between carrier and the laser mode, parameter  (DDF) in Eqs.(3) play an important role to normalize the intensity of laser field and the delay time. So, we can use this theoretical model to study the turn-on dynamical of InGaAs/GaAs QD laser to obtain results which are in agreement with experimental data [Marius Grundmann (2000), M. Grundmann (2000), and  Matthias Kuntz (2006)].

The pump rate  is either a constant value in case of pulsed excitation of the time-dependent pump pulse, or in the case of CW excitation [Christopher Gies, et. al. (2008)]

Where  is the pump pulse area, which is directly corresponds to the number of two-level systems excited by the pulse.  is a pulse duration (pulse width).

The MEM (1)−(4) provide convenient methods to fit the input/output characteristics of QD microcavity lasers. The calculations are based on producing a curve of photon population against pump rate in Fig.2 for pump pulses shorter than the spontaneous emission time, which represents InGaAs/GaAs QD laser input/output curve. By using this figure especially, the operation threshold pump rate can be obtained at the curve jump, i.e. one have   in this figure. The re-absorption present in the system modifies the height of the jump. The upper branch of the input/output curve can be masked to an extent where the threshold is not even fully developed.

Figure 2: Steady-State input-output characteristic of InGaAs /GaAs QD laser with wavelength of 1.3μm: Simulated PP vs. Pump Rate . The threshold Pump Rate is determined from the extrapolated laser onset if spontaneous emission is neglected. The used parameters are ordering in Table (1).

Table(1): The used parameters of InGaAs /GaAs QD laser with wavelength of 1.3 μm which are taken from Ref.[ Christopher Gies, et. al. (2007)].

| Unit | Value | Symbol |
| --- | --- | --- |
| μeV | 20. | k |
| μeV | 6. | C |
|  | 0.02 | β |
| ps | 1. |  |
| ps | 5. |  |
| ps | 50. |  |
| fs | 2. |  |
| ps | 10 |  |
|  | 10 |  |
| ps−1 | 3.146 |  |
|  | 20 |  |

The QD laser dynamics in this model are based on the following; the laser microcavity of QD can be considered as a four level system (see Fig.1) where holes have two levels (s- and p-shell) in valence band and electrons have two levels (s- and p-shell) in conduction band. QD Laser procedure includes the direct pumping between p-shell holes to p-shell electrons, then through equilibrium transition between holes state, i.e. holes rise from p-shell to the s-shell in valence band and electrons relaxes from p-shell to s-shell in conduction band. The laser operation occur through the recombination process between descending captured electrons from s-shell and capture of rising holes from s-shell, then the light is emitted. Each of the six variables in the model under investigation has its own dynamics.

The dynamical delay factor play very clear role to determine the characteristics of QD laser. Such as the field and the delay time of QD laser output are dependent on it. Fig.3. represents the variation of photon population and the delay time as a function of this factor.

(a)

Figure 3: Characteristic of InGaAs /GaAs QD laser with a wave-length of 1.3 µm varying with DDF change: (a) Steady-State of PP vs. DDF, (b) Delay Time vs. DDF. Continues

(b)

Continued

So clear, both quantities are dependent to DDF region of variation (10−30 100). By controlling on the dynamical interaction between lasing state carriers  and the laser mode, the parameter DDF play an important role to determent the laser characteristics. From the above figure, it's clear that  the output field is linearly increases and the delay time increases also nonlinearly with decreasing DDF in scale (10−10  100). According to the obtained results, we have chosen the value  for DDF in all our results in this work.

The rate of photons in the laser mode leaving the cavity is given by . For pulsed excitation, the PP changes dynamically, and the time-integrated emission rate is  yields the total PP emitted from the laser mode [Christopher Gies, et. al. (2008)]. The tilde denotes the PP outside the cavity, the total number of excited systems is given again by the time integral over  , yielding . In a CW case, the situation is somewhat different. The system is excited at a constant rate, and after the switch-on dynamics, a stationary state is reached, where the rate of emitted photons per time is constant. The signal at the detector is nevertheless integrated over a time window τ so that the collected PP  scales directly with the integration time [Christopher Gies, et. al. (2008)].The excitation takes place at a constant rate, and the total number of two-level excitations scales again with the integration time τ of the measurement. Thus,  and    can be compared only up to a scaling factor τ. The same argument holds for the pump rate at which two-level systems are excited [P. R. Eastham, et. al. (2006) and W. Pِtz; (2008)].

In order to discuss the results of our simulation in the case of CW excitation we compare the time evolution of the simulated p-shell populations (QD pump states) illustrated in Fig.4(a) and (b)  with the time behavior of s-shell populations (QD lasing states) represented in Fig.4(c) and (d).

| (a) | (b) |
| --- | --- |
| (c) | (d) |

Figure 4 Turn-on dynamic of InGaAs /GaAs QD model carriers population calculated from MEM (1) – (2): (a) and (b) Population of p-shall carriers  (pump states of electron /hole, respectively), (c) and (d) Population of s-shall carriers  (lasing states of electron/ hole, respectively).

A characteristic feature of QD lasers is the strongly damped relaxation oscillation showing only one pronounced peak with a full width at half maximum. Fig.5 shows the PAP and PP variation with time. It is quite clear that a delay time occur followed by a transient region, then the steady state of the laser output. Fig.5 (a) and (b) represents a comparison of the behavior of PAP and PP. The way by which the PAP follows the variations of the electro-magnetic field (photon population) where the former is a function of the later suggest the correctness of the obtained results for the parameters used in this work. By choosing two different C values two behaviors are obtained for the PAP and PP values, i.e. the PAP need not to follow exactly the variation of PP, as can be seen in Fig.5 (c) and (d).

To gain insights to the relation between the above mentioned six – variables, we have plotted the relation among  with  or  as can be seen in Figs.6(a) and (b), respectively. The figure represents another comparison between PP, PAP and  with time.

| (a) | (b) |
| --- | --- |
| (c) | (d) |

Figure 5: Turn-on dynamic of: (a) PAP and (b) PP, with ,  (c) and (d) The same variables with  .Other parameters as in Fig.2

(a)

Figure 6: Turn-on dynamic of PP (a.u.) corresponding with: (a) Population of pump states , (b)Population of lasing states . The other parameters as using in Fig.5(c).

Continued

(b)

Continued

Discussion and Conclusion

To study the turn-on dynamics and relaxation oscillations in the InGaAs /GaAs QD laser with a wavelength of 1.3 µm, one get a poor agreement with experimental results When one use the theoretical model of laser for semiconductor QDs [Christopher Gies, et. al. (2008)], (see Fig.A1 in Appendix)

The addition of DDF in to the MEM  by Gies et.al, making a good normalize of this model to study the turn-on dynamical characteristics of semiconductor QD laser. That is very clear the effect of increase the p-doped (increase the DDF) on the QD laser dynamics in delay time and intensity of laser field. Our specific results of turn-on dynamics of InGaAs/GaAs QD semiconductor laser output at room-temperature CW lasing with a wavelength of 1.3μm are studied. That is shown in: delay time, transient rise time, length of transient region, number of oscillations in the transient region, delay time to reach steady state, level of output in the steady state.

we can use the theoretical model with DDF to study the turn-on dynamical of InGaAs/GaAs QD laser to obtain results which are in agreement with experimental data [Marius Grundmann (2000), M. Grundmann (2000), and  Matthias Kuntz (2006), Ermin Mali´c, et. al. (2007)] (see Fig.A2 in Appendix). For this model, the PAP is a function of PP but not always need to follow the variation of PP exactly. So the carrier populations of pumping ∕ lasing states are studied her. The system of QD lasers dynamics can be modeled extremely well by this mentioned of model equations.

Appendix

Figure A1: Switch-on oscillations of the carrier (dotted line: s-shell, dashed line: p-shell) and photon population in the laser mode(solid line) [Christopher Gies (2008)].

Figure A2:  Experimental result for an InAs/GaAs QD laser with a wavelength of 1.3 µm [Ermin Mali´c, et. al.(2007)]

References

Christopher Gies, Jan Wiersig, Michael Lorke, and Frank Jahnke; 2007, Physical Review A, 75: 013803(1-11).

Christopher Gies, Jan Wiersig, and Frank Jahnke; 2008, Physical Review Letters, 101: 067401(1-4).

Christopher Gies; 2008, PhD. thesis, University of Bremen, Berlin, Germany

Chun-Hua Yuana and Ka-Di Zhu; 2006, Applied Physics Letters, 89: 052115(1-3),

Emmanuel Rosencher and Borge Vinter; 2004, “Optoelectronics”. ©Cambridge University, Press, English edition.

Ermin Mali´c, Moritz J. P. Bormann, Philipp Hovel, Matthias Kuntz, Dieter Bimberg, Andreas Knorr, and Eckehard Scholl; , 2007, “Coulomb damped relaxation oscillations in semiconductor quantum dot lasers”. IEEE Journal of Selected Topics in Quantum Electronics, 13(5): 1242- 1248.

Martin J. Stevens, Robert H. Hadfield, Robert E. Schwall, Sae Woo Nam, and Richard P. Mirin; 2006, IEEE Journal of Selected Topics in Quantum Electronics, 12(6): 1255-1268.

Marius Grundmann; 2000, Applied Physics Letters, 70(10): 1428 – 1430.

M. Grundmann, 2000, IEEE Electronics Lettes, 36(22): 1851-1852.

M. Lorke, T. R. Nielsen, J. Seebeck, P. Gartner, and F. Jahnke; 2006, Physical Review B, 73: 085324(1-10).

Matthias Kuntz; 2006, PhD. thesis, Technische Universit´at Berlin, Berlin, Germany.

N. Baer, C. Gies, J. Wiersig, and F. Jahnke; 2006, The European Physical Journal B, 50: 411-418.

Paul Harrison; 2005, “Quantum Wells, Wiresand Dots: Theoretical and Computational Physics of Semiconductor Nanostructures”. ©John Wiley & Sons Ltd., The Atrium Southern Gate, Chichester.

Peter Michler; 2003,  “Single Quantum Dots, Fundamentals, Applications, and New Concepts”. © Springer-Verlag Berlin Heidelberg.

P. R. Eastham and P. B. Littlewood; 2006, Physical Review B, 73: 085306(1-11).

Ryan R. Alexander, David T. D. Childs, Harsh Agarwal, Kristian M. Groom, Hui-Yun Liu, Mark Hopkinson, Richard A. Hogg, Mitsuru Ishida, Tsuyoshi Yamamoto, Mitsuru Sugawara, Yasuhiko Arakawa, Tom J. Badcock, Richard J. Royce, and David J. Mowbray; 2007, IEEE Journal of Quantum Electronics, 43 (12): 1129–1139,

T. Feldtmann, L. Schneebeli, M. Kira, and S. W. Koch; 2006, Physical Review B, 73: 155319(1-13).

Todd Steiner; 2004,  "Semiconductor Nanostructures for Optoelectronic Applications”. © ARTECH HOUSE, INC.,

T. R. Nielsen, P. Gartner, and F. Jahnke; 2004, Physical Review B, 69: 235314(1-13).

Swati Ramanathan; 2007, “Polarization studies of coupled quantum dots”. MSc. thesis, Department of Physics and Astronomy, College of Arts and Sciences, Ohio University, USA.

Voicu Popescu, Gabriel Bester, and Alex Zunger; 2009, Applied Physics Letters, 95: 023108(1-3).

W. Pِtz; 2008, Physical Review B, 77: 035310(1-5).