Optical  Perspective  of the Fourier Transformers

Hakiema Salman Jabor       Reyadh  Naji  Ali

Babylon University - College of Science for Woman, Iraq

Yaseen Hasan Kadhim

Babylon University - College of Science, Iraq

Abstract

The present work is a theoretical and experimental study of a biconvex lens as an optical processor .The MATLAB software concerning the Fourier optics  is used as the basic numerical tool for these work. In addition to providing functions for calculating  Fraunhofer  diffraction .  The  FFT  command  enables  the calculation  of  the  diffraction  pattern  of  an  arbitrary  aperture . Relatively simple MATLAB ®  scripts are constructed to calculate the diffraction patterns of arbitrary graphics such as geometry shapes, pictures of faces, letters .This paper also describes a few demonstrations that can be used to reinforce what is covered on the work . The demonstrations are based on a simple (2F set-up )  system. Diffractive imaging relies on many other technological innovations , including : a CCD camera ,digital  camera HD (12 Mega Pixels) with a lens  (f=7.23mm). The experimental results  agree with the theoretical calculations .

الخلاصة

تم في هذا البحث دراسة نظرية وعملية باستخدام عدسة محدبة الوجهين كمعالج إشارة بصرية . في هذا العمل تم استخدام برامجيات  MATLAB كأداة لإجراء الحسابات النظرية الخاصة بحسابات دوال فتحات الحيود وأنماطه  . بالإضافة إلى توفير الدوال لحساب حيود فرانهوفر ,  تمكننا  FFT من حساب أنماط الحيود لفتحة اعتباطية . بنص بسيط مكتوب بلغة MATLAB ®  لحساب أنماط الحيود  لإشكال اعتباطية مثل أشكال هندسية , صور وجوه , أحرف . هذا البحث يصف أيضا عدة  إثباتات يمكن استخدامها لدعم هذا العمل . هذه الإثباتات تستند على أساس استخدام منظومة 2F . صور الحيود تعتمد على عدة طرق تكنولوجية , من ضمنها : كاميراCCD , كاميرا  رقمية HD  ( 12ميكا بكسل)  بعدسة  بعدها البؤري  (f=7.23mm). والنتائج العملية متطابقة مع النتائج النظرية .

1- Introduction

Diffraction theory is often taught as a purely mathematical treatment or used to analyze very simplistic apertures such as slits and holes. The effect is a general characteristic of wave phenomena occurring whenever a portion of a wavefront, be it sound, a matter wave, or light, is obstructed in some way. The various segments of the Wavefront that propagate beyond the obstacle interfere, causing the particular energy-density distribution referred to as the diffraction pattern. There is no significant physical distinction between interference and diffraction (Eugene Hecht , 2002).                      As shown in figure (1) .

The goal of this paper is to describe how the scientific analysis tool MATLAB® can be used to perform complex mathematical calculations with  Fraunhofer diffraction domains and experimental implementation . Fraunhofer diffraction deals with the limiting cases where the light appoaching the diffracting object is parallel and monochromatic, and where the image plane is at a distance large compared to the size of the diffracting object (Okan K. Ersoy , 2007) .  Fraunhofer diffracton is  far ﬁeld approximation, where the observe pattern in the focal plane of a lens  . The far ﬁeld diffraction, or Fraunhofer diffraction of the Kirchhoff–Fresnel integral have the same mathematical appearance . The only difference is that in far ﬁeld approximation the diffraction pattern is observed on a faraway screen, whereas in Fraunhofer diffraction the observation screen is placed at the focal plane of a lens and that may be closer to the aperture (K.D. Moller   et al. , 2003).  Linear transforms , especially Fourier and Laplace transforms, are widely used in solving problems in science and engineering. The Fourier transform is used in linear systems analysis, antenna studies, optics, random process modeling, probability theory, quantum physics,  and  boundary-value problems (Brigham , E.Oren ,1988) and has been very successfully applied to restoration of astronomical data (Brault,J.W.andWhite,O.R , 1971) .

2- Theory

Fraunhofer diffraction is the theory of transmission of light through apertures under the assumption that the incident  wave is multiplied by the  aperture function . Fraunhofer diffracton is  far ﬁeld approximation , where the observed  pattern is located at  the focal plane of a lens  (Okan K. Ersoy , 2007) , which usually called Fourier plane . So , we will use  the fraunhofer approximation to determine the propacation of light in the free space beyond the aperture . As shown  in figure (2)  , in this figure which showing  position of   Fraunhofer (far ﬁeld) region               (Keigo Iizuka , 2008) .

In fig ( 3 ) where the  observed  plane wave which is diffracted in one plane . For this wave in the  plane directly behind the plane  with the following transmission distribution (David Voelz , 2011) : -

Where   : electric field distribution of the incident wave. The  further  expansion  can  be  described  by  the  assumption that a spherical wave emanates from each point  behind the  diffracting  structure  (Huygens’  principle).  This  lead  to Kirchhoff’s diffraction integral (David Voelz , 2011) : -

Equation  (2)  corresponds  to  a  accumulation  of  spherical waves, where the factor    is a phase and amplitude factor and  a directional factor which results from the Maxwell field equations. The Fresnel approximation (observations in a remote radiation field) considers only rays which occupy a small angle to the optical axis  . In this case, the  directional  factor  can  be  neglected  and  the   dependence  becomes :   . In  the  exponential  function ,  this cannot be performed as easily since even small changes in  result in large phase changes. This results in the Fresnel approximation of the diffraction integral .

For long distances from the diffracting plane with concurrent finite  expansion  of  the diffracting  structure , will  obtain  the Fraunhofer approximation  as given by eq. (4).

Where    is the phase factor and is the electric field distribution in the plane    for  (David Voelz , 2011) .

3- Theoretical Results

When the distance away from the grating is large or a lens is used to focus the diffraction pattern to the image plane then the diffraction pattern becomes a Fourier transform as given by (Joseph W. Goodman , 1996) .

:  is the electric field distribution .                                                                                                  
  :  is the phase factor .

and   are spatial frequencies.

=  wave length .

3-1  Fourier Transform using Matlab  for  rect-function

The  one-dimensional  (1-D)  rectangular  function   is given by : -

Where () is the domain of the function (or the width of the  aperture) .The two-dimensional of the rectangular function is given by : -

The  Fourier  transform  of  the  (2-D)  rectangular  function is given by (Ting  Chung Poon , 2007 ) : -

The aperture  function , { rect}  and its Fourier transform is shown in fig. (4).

3-2 The Triangle Function

The triangle function is a shape  like a triangle, as its name indicates. Figure (5: a) illustrates the wave form. The function can be obtained by the convolution of  with itself  as shown (Keigo Iizuka , 2008) .

Using the fact : -

the Fourier transform of eq. (9) is found to be in  (Fig. 5: b)

3-2-1  Fourier Transform of Bitmap Images

When the (2-D) function or image is given with a bitmap file, we can use the     m-file  given  in  algorithm ( 1)  to  find  its  Fourier  transform.  Figure ( 6 : a)  is  the bitmap image used when the image file of the size is (256256) . It is easily generated with Microsoft® Paint. Figure (6:b) is the diffraction pattern (or the Fourier transform) of the tri-function (Ting  Chung Poon , 2007 ) .

Algorithm 1: fft2D bitmap_image.m : m-file for 2-D Fourier transform of  bitmap image.

----------------------------------------------------------

%fft2Dbitmap_image.m

%Simulation of Fourier transformation of bitmap images

clear

I=imread('triangle.bmp','bmp'); %Input bitmap image

I=I(:,:,1);

figure(1)  %displaying input

colormap(gray(255));

image(I)

axis off

FI=fft2(I);

FI=fftshift(FI);

max1=max(FI);

max2=max(max1);

scale=1.0/max2;

FI=FI.*scale;

figure(2)  %Gray scale image of the absolute value of transform

colormap(gray(255));

image(10*(abs(256*FI)));

axis off

-------------------------------------------------------

3-3  Element Size

The extent of the diffraction pattern is complementary to the size of the single

diffracting elements . Figure  (8) shows this reciprocal behavior using  elliptical     apertures of different size (Cetin, A.E. , et al. , 2004) .

4- Experimental Results

The experimental results include  investigation of the Fourier transform by a convex lens for different diffraction objects in a ( 2F set-up) system . As shown in 	figure (12).

The diffraction pattern of a rectangular aperture by using a digital camera  and CCD camera as shown in figures (13,14,15,16) .

The diffraction pattern of a triangular  aperture by using a digital camera  and CCD camera as shown in figures (17,18,19,20) .

5- Conclusions:

We conclude the  diffraction  pattern  which we  calculated  with fft2  method, the number of pixels in the diffraction pattern is equal to the number of pixels in the initial image , as shown in figures ( 4,6,8,9,10,11 ) . obviously , the total extent of the image is increased without changing the slit or hole width by adding space around  the  image,  which  is  called  zero  padding. In figures ( 13,14,17,18) these figures taken   with spatial filter , recorded by a digital  camera , from this figures we notice that

the intensity pattern observed varies with the distance from the aperture . In figures

(5,16,19,20) , recorded by a CCD  camera ,  as seen the  diffraction  pattern  depends on the size of aperture or element size . So, the experimental results  agree with the theoretical calculations .

References

Brault , J. W.and  White, O. R , (1971) " The analysis and restoration of astronomical

data via the fast Fourier transform", Astron. & Astrophys .

Brigham , E . Oren , (1988) " The Fast Fourier Transform and Its  Applications " ,

Prentice-Hall, Inc. .

Cetin, A.E. , et al. , (2004  ) " Signal recovery  from  partial  fractional  Fourier transform  information " , IEEE , PP : 217-220  .

David Voelz  , (2011) "Computational Fourier Optics " ,  A Matlab® Tutorial , Spie

Press .

Eugene Hecht , (2002) "Optics", 4th  ed , Addison Wesley .

Joseph W. Goodman , (1996) " Introduction to Fourier Optics " , 2nd ed , Mc Graw

–Hill .

Keigo Iizuka , (2008) " Engineering Optics " , 3rd  ed ,  Springer  .

K.D. Moller , et al. , (2003)  ," Optics : Learning by Computing , with Examples Using Mathcad® " , Springer .

Okan K. Ersoy, (2007) , " Diffraction,  Furrier Optics and Imaging " , Wiley .

Ting  Chung Poon , (2007) "Optical Scanning Holography With Matlab®", Springer .

# Text boxes

Fig . 1 : Arrangement  used  for  observing diffraction of  light  (Joseph W. Goodman , 1996).

Fig . 3 :  A  plane  wave   is  diffracted  in  the  plane  with  for  (David Voelz , 2011).

Fig . 2 :  Diagram showing the relative positions  of  the Fresnel  (near  ﬁeld)  and Fraunhofer (far ﬁeld) regions (Keigo Iizuka , 2008) .

Fig . 12 :  Experimental (2F set-up) system .

Fig . 13 : Rectangular aperture recorded with a digital camera .

Fig . 4 : a -  rect- function: gray-scale plot .

Fig . 4 : b - Square-absolute value of Fourier transform of the rect- function: gray-scale plot .

Fig . 4 : c- Square-absolute value of Fourier transform of a rect- function: cross-section plot.

Fig . 4 : d-  The  power distribution of a rect- function  by 3-D .

Fig . 6 : a- Bitmap image of a triangular  aperture  function.

Fig . 6 : b- The diffraction pattern (or the Fourier transform) of the tri-function .

Fig . 6 :  Bitmap image and its transform generated using the m-file in Matlab software .

Fig . 7: a- Bitmap image of a face.

Fig . 7: b- Displaying the absolute value of the transform of a .

Fig . 7 :  Bitmap image and its transform generated using the m-file in Matlab software  .

Fig . 8: Bitmap images and its transform generated by the m-file in the Matlab software for different size elliptical  apertures.

Fig . 4 :  Rect- function and its Fourier transform .

Fig . 5:  (a) Triangle function  and (b) its Fourier transform  (Eugene Hecht , 2002)  .

Fig .  17 :  The  power distribution in the  triangle aperture as shown by a digital  camera HD.

Fig . 18 :  Diffraction pattern of triangle aperture  as shown by a digital camera HD.

Fig . 9: Diffraction pattern  of the letter(T- aperture) made with times new roman fonts .

Fig . 10: Diffraction pattern  of the letter (T- aperture) made with  an arial font .

Fig . 11: Diffraction pattern of an aperture constructed with (QTR) letters.

Fig . 14 :   Diffraction pattern of rectangular recorded with a digital camera .

Fig . 15 : Power distribution in rectangular aperture  recorded with a CCD  camera .

Fig . 16 :   Diffraction pattern of rectangular recorded  with a CCD  camera .

Fig .  19 :  The  power distribution in the  triangle aperture as shown by a CCD    camera .

Fig . 20 :  Diffraction pattern of triangle aperture  as shown by a CCD  camera .

F.T.

F.T.

F.T.

F.T.

F.T.

F.T.

F.T.

F.T.

F.T.