Study the Geotechnical characteristic for the soil of Wasit Electrical station by using The Downhole Seismic velocity logging method

Ali Q. Yahya,

University of Baghdad, College of Science, Department of Geology.

Abstract

The Downhole Seismic velocity logging (DS) was used for the first time in Iraq. It is one of the bore hole seismic methods and it was conducted on January 25th 2010 in two drilled boreholes (WVT1 and WVT2) of 60 meters depth each. These boreholes located in area which was selected to build an electrical generating station in Wasit governorate, Iraq. The purpose of the survey is to know the geotechnical characteristics of the subsurface soil layers in that area. The first arrival time, of the P-wave and S-wave, was measured for each meter downward till 59 meters for each well separately. The picking of the first arrival times was done for the 118 seismic records (59 records for WVT1 and 59 records for WVT2). At each depth the travel time of the first arrival for three components were measured. These are P-wave, S-wave vertical and S-Wave horizontal (with 90o angles between them). The picking was done using the Terraloc instrument software in addition to ReFlexw ver. 4 software and from the first arrival the P-wave and S-wave velocities were concluded which are related to the important geotechnical elastic constants of Poisson’s ratio, shear modulus, bulk modulus, and Young’s modulus. By knowing the density (from the boreholes tests data) then the elastic – dynamic modulus and constants for the subsurface soil layers had been determined. The measurement results for WVT1 and WVT2 plotted as curves (velocity verses depth) in addition to the borehole lithology (stratigraphic column). The lithology, or the stratigraphic columns of the nearest boreholes (BH 126 and BH 137) were used to compare with the results of seismic measurements. There was very good relation between the seismic results and the lithology However, it seems that the Vp and Vs curves show more details than the stratigraphic logs of these boreholes itself, also there was convergence between them and the results of the SPT test which were done in this area.

الخلاصة

تم أستخدام طريق الجس الزلزالي البئري لأول مرة في العراق.تعتبر  هذه الطريقة من الطرق الزلزالية الابارية وقد تم أنجازالعمل الحقلي في 25/1/2010 في بئرين محفورين هما (WVT1 و WVT2) ذو عمق 60 متر لكل بئر. هذه الابار تقع في منطقة أختيرت لبناء محطة توليد الطاقة الكهربائية في محافظة واسط، العراق. الغرض من هذا المسح هو لمعرفة الصفات الجوتكنيكية لطبقات التربة التحت سطحية في تلك المنطقة. زمن الوصول الأول ،للموجات (P) و(S)، تم قياسه لكل متر بأتجاه الأسفل لغلية عمق (59) متر لكل بئر بصورة منفصلة. الألتقاط  لأزمان الوصول الأول تم عمله ل(118) تسجيل زلزالي بواقع (59) تسجيل للبئر(WVT1) و(59) تسجيل للبئر(WVT2). لكل عمق  فأن زمن الأنتقال للوصول الأول للمركبات الثلاثة قد تم قياسه. هذه المركبات هي موجة ال(P)، موجة ال(S) العمودية وموجة ال(S) الأفقية مع زاوية (°90) بين المركبات الثلاثة. الألتقاط قد تم بأستخدام برنامج جهاز ال(Terraloc) بالأضافة الر برنامج (ReFlexw ver. 4) ومن زمن الوصول الأول تم أستنتاج سرع موجات ال (P) و (S) والتي هي متعلقة بالمعاملات الجيوتكنيكية المهمة التالية: نسبة بويسون، معامل القص، معامل بولك ومعامل يونك. بمعرفة الكثافة لطبقات التربة التحت سطحية، من خلال بيانات فحص الابار، نستطيع حساب معاملات المرونة الديناميكية لطبقات التربة التحت سطحية. نتائج القياسات الزلزالية للبئرين (WVT1) و (WVT2) تم رسمها على شكل منحنيات (سرعة مقابل عمق) بالأضافة الى ليثولوجية الابار(العمود الطباقي). الليثولوجية أو الأعمدة الطباقية للأبار الأقرب للبئرين (WVT1) و (WVT2) والتي هي (BH126  و BH137) تم أستعمالها للمقارنة مع نتائج القياسات الزلزالية. كانت هناك علاقة جيدة جدا بين النتائج الزلزالية والليثولوجية. كما أن منحنيات سرع الموجات الزلزالية (P) و (S) أظهرت تفاصيل أكثر من السجلات الطباقية للابار نفسها، كذلك كان هناك تقارب بين هذه المنحنيات ونتائج فحص الأختراق القياسي للتربة (SPT) في هذه المنطقة.

Introduction

Downhole seismic velocity logging (DS) is a well known method of measuring seismic wave velocity profiles, and has been used for more than 50 years. It is the simplest and cheapest method in the suite of borehole seismic techniques, as it requires only a single borehole (figure 1).  This methods relies on a surface source to generate primary (p) waves and secondary (s) waves that travel down the soil or rock column where they recorded by a special borehole geophone which is lowered and locked in the borehole at specific depth (1). This geophone contains three components: One vertical component that is for P-Wave detection, while the other two components are for S-Wave detection. They form a horizontal cross inside the lowered tube. In this case the P-Wave and S-Wave will be recorded independently. Travel time is measured using a trigger at the surface, and a digital seismograph recording. The propagation of seismic waves is controlled by the parameters of rock elasticity and density. By measuring of the time intervals between the generation of pulse and its reception at the geophone at various distances give the velocity of propagation of the pulse in the ground. By knowing the density (from the boreholes tests data) then the elasto–dynamic modulus and constants for the subsurface soil layers can be determined (2). Typical applications of (DS) include: Dam safety investigations, Seismic site response studies for (bridge abutments, dams, buildings, etc.), Foundation studies, Measurement of soil/rock properties (i.e. shear modulus, bulk modulus, compressibility, and Poisson’s ratio), Characterization of strong motion sites and velocity control for seismic reflection surveys.  Beside that the (DS) is a reliable choice for certain situations such as:

1-can work in borehole diameters as small as 2 inches (cased)

2- Can be good choice when high resolution is not important and borehole depth is shallow

3-when validation is desired for Suspension P-S velocity logging results, which is another method of borehole seismic methods and consider a relatively new method of measuring seismic wave velocity profiles; the (DS) is a good choice because it measures velocities in the same orientation (1), (2).

(figure-1-) the downhole seismic method

The Field Work

This method is performed in accordance with Standard Test Methods for Downhole Seismic Testing (ASTM D7400 – 08), (3). The field work was carried out using the 24 channels seismic refraction system (ABEM Terraloc MK6 system, Sweden made), (figure-2a).This instrument is connected to multi-component borehole geophone (BGK3, geotomographic, Germany made), (figure-2b), by cable of 150 meters length.

The multi-component geophone tube is equipped with pneumatic clamping unit serves to anchoring the geophone inside the borehole for seismic recording. It consists of a plastic pipe perforated by several holes and bearing a rubber hose. When air is pressed into the clamping unit, the rubber expands in direction to counter side the reference direction. After reaching the wall of borehole the geophone probe is pressed against the wall. By further increasing of the pressure the geophone probe can be anchored in the borehole for seismic recording. The borehole diameter should be less than 10 cm to make the right anchoring. Unfortunately the borehole diameter in this study was more than 20 cm. Therefore external plastic tube was attached to the BGK3 tube, which makes the anchoring possible even for borehole diameter more than 28 cm. With this attachment the right anchor situation was reached during the seismic measurements (figure-3) In addition the BGK3 borehole geophone is equipped by electronic hand-held compass. This compass gives the direction of the horizontal components (S-Wave) relative to the north. Accordingly the right direction of these components can be identified and the BGK3 can be rotated to the desire direction before the anchoring to the borehole wall.

(Figure-2) The left picture is the ABEM Terraloc MK6 system and the right picture is the borehole geophone BGK3.

The survey was conducted on January 25th 2010. It was in two drilled boreholes (WVT1 and WVT2) of 60 meters depth each. The first measurement was started at depth of 2 meters from the surface and then continued stepwise of one meter down to a depth of about 59.5 meters. At each depth the travel time of the first arrival for three components were measured. These are P-wave, S-wave, and S-Wave (with 90o angles between them).The energy source was a hammer impacts. The weight of the hammer is about 12 kg. The impacts were on the surface away from the borehole by a distance of 5.0 to 6.0 meters. During the measurements we tried to avoid all type of artificial noises. The noise level can be monitored easily on the Terraloc main screen. However, some of the measurements were repeated more than once because of the noises.

(Figure-3)  the bore hole with the cable of the geophone and the set of the measurement.

Data processing

The picking of the first arrival times was done for the 118 seismic records (59 records for WVT1 and 59 records for WVT2). The picking was done using the Terraloc instrument software in addition to ReFlexw ver. 4 software. The velocities of P-Wave and S-wave were calculated depending on the first arrival and the known distance between the hammer impacts and the geophone depths. The first arrival here will correspond to the seismic wave travel time between the energy source and the geophone. The elasto – dynamic modulus and constants of subsurface soil layers (seismic layer) were calculated using the recorded P-wave and S-wave velocities and the densities. The densities values were deduced from the closes borehole chart. Unfortunately this borehole chart shows densities value down to a depth of 12 meters only. Accordingly our first

Calculation was to this depth for both WVT1 and WVT2. We have used the nature density value in our calculation. It was calculated from the dry density and the moisture content percent. For depths more than 12 meters however, the natural density was estimated 19.5 KN/m3 for the sand silty layers. It was deduced from the specific gravity values. The related familiar equations, which listed below, were used for elastic modulus calculations.

(1)

(2)

(3)

(4)

Where:

is the Poisson's ratio, is the velocity of the primary waves, is the velocity of the secondary waves, E is the Young modulus,  is the density of the medium, G is the Shear modulus, K is the Bulk modulus (4)

Results

Table -1 and table -2 shows the P-wave and S-Wave velocities and the parameters which were calculated using these velocities data for WVT1 and WVT2 respectively.

Table-1- represents the VSP and the calculated elastic modulus for the borehole WVT1.

| D(m) | Vp (m/sec) | Vs (m/sec) | Unit weightKN/m2 | Poisson’s Ratio | Young Modulus (MPas) | Bulk Modulus (MPas) | Shear Modulus (MPas) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2 | 527.046 | 287.48 | 19.798 | 0.28824 | 4.21562 | 3.31785 | 1.6362 |
| 3 | 559.017 | 304.918 | 20.359 | 0.28824 | 4.87696 | 3.83834 | 1.89288 |
| 4 | 554.7 | 300.463 | 20.581 | 0.29238 | 4.80251 | 3.85527 | 1.85801 |
| 5 | 650.854 | 300.394 | 20.581 | 0.36466 | 5.06879 | 6.24213 | 1.85716 |
| 6 | 606.092 | 353.553 | 19.682 | 0.24211 | 6.11178 | 3.94979 | 2.46025 |
| 7 | 576.222 | 354.598 | 19.682 | 0.19524 | 5.91597 | 3.2353 | 2.47481 |
| 8 | 625 | 333.333 | 19.682 | 0.30124 | 5.69134 | 4.77243 | 2.18689 |
| 9 | 772.618 | 386.309 | 19.734 | 0.33333 | 7.85333 | 7.85333 | 2.945 |
| 10 | 832.993 | 448.535 |  | 0.29583 |  |  |  |
| 11 | 894.997 | 481.922 |  | 0.29583 |  |  |  |
| 12 | 958.315 | 447.214 | 19.775 | 0.3608 | 10.7639 | 12.8874 | 3.955 |
| 13 | 894.864 | 447.432 | 19.50 | 0.33333 | 10.4102 | 10.4102 | 3.90381 |
| 14 | 1087.97 | 585.829 | 19.50 | 0.29583 | 17.3442 | 14.1586 | 6.69231 |
| 15 | 1009.72 | 621.365 | 19.50 | 0.19524 | 17.9975 | 9.8424 | 7.52885 |
| 16 | 1068 | 657.231 | 19.50 | 0.19524 | 20.1352 | 11.0114 | 8.42308 |
| 17 | 1001.54 | 600.925 | 19.50 | 0.21875 | 17.1641 | 10.1713 | 7.04167 |
| 18 | 1185.85 | 592.927 | 19.50 | 0.33333 | 18.2813 | 18.2813 | 6.85547 |
| 19 | 1245.36 | 711.602 | 19.50 | 0.22878 | 24.2668 | 14.9121 | 9.87436 |

| D(m) | Vp (m/sec) | Vs (m/sec) | Unit weightKN/m2 | Poisson’s Ratio | Young Modulus (MPas) | Bulk Modulus (MPas) | Shear Modulus (MPas) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2 | 527.046 | 287.48 | 19.798 | 0.28824 | 4.21562 | 3.31785 | 1.6362 |
| 3 | 559.017 | 304.918 | 20.359 | 0.28824 | 4.87696 | 3.83834 | 1.89288 |
| 4 | 554.7 | 300.463 | 20.581 | 0.29238 | 4.80251 | 3.85527 | 1.85801 |
| 5 | 650.854 | 300.394 | 20.581 | 0.36466 | 5.06879 | 6.24213 | 1.85716 |
| 6 | 606.092 | 353.553 | 19.682 | 0.24211 | 6.11178 | 3.94979 | 2.46025 |
| 7 | 576.222 | 354.598 | 19.682 | 0.19524 | 5.91597 | 3.2353 | 2.47481 |
| 8 | 625 | 333.333 | 19.682 | 0.30124 | 5.69134 | 4.77243 | 2.18689 |
| 9 | 772.618 | 386.309 | 19.734 | 0.33333 | 7.85333 | 7.85333 | 2.945 |
| 10 | 832.993 | 448.535 |  | 0.29583 |  |  |  |
| 11 | 894.997 | 481.922 |  | 0.29583 |  |  |  |
| 12 | 958.315 | 447.214 | 19.775 | 0.3608 | 10.7639 | 12.8874 | 3.955 |
| 13 | 894.864 | 447.432 | 19.50 | 0.33333 | 10.4102 | 10.4102 | 3.90381 |
| 14 | 1087.97 | 585.829 | 19.50 | 0.29583 | 17.3442 | 14.1586 | 6.69231 |
| 15 | 1009.72 | 621.365 | 19.50 | 0.19524 | 17.9975 | 9.8424 | 7.52885 |
| 16 | 1068 | 657.231 | 19.50 | 0.19524 | 20.1352 | 11.0114 | 8.42308 |
| 17 | 1001.54 | 600.925 | 19.50 | 0.21875 | 17.1641 | 10.1713 | 7.04167 |
| 18 | 1185.85 | 592.927 | 19.50 | 0.33333 | 18.2813 | 18.2813 | 6.85547 |
| 19 | 1245.36 | 711.602 | 19.50 | 0.22878 | 24.2668 | 14.9121 | 9.87436 |

| 20 | 1230.47 | 734.785 | 19.50 | 0.22288 | 25.7495 | 15.4863 | 10.5282 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 21 | 1560.02 | 780.012 | 19.50 | 0.33333 | 31.6378 | 31.6378 | 11.8642 |
| 22 | 1900.29 | 950.146 | 19.50 | 0.33333 | 46.9444 | 46.9444 | 17.6042 |
| 23 | 1697.84 | 914.22 | 19.50 | 0.29583 | 42.2392 | 34.481 | 16.2981 |
| 24 | 1767.05 | 951.486 | 19.50 | 0.29583 | 45.7529 | 37.3493 | 17.6538 |
| 25 | 1606.87 | 918.211 | 19.50 | 0.25758 | 41.3508 | 28.4287 | 16.4407 |
| 26 | 1905.95 | 952.976 | 19.50 | 0.33333 | 47.2245 | 47.2245 | 17.7092 |
| 27 | 1728.66 | 987.801 | 19.50 | 0.25758 | 47.8563 | 32.902 | 19.0271 |
| 28 | 1789.73 | 954.521 | 19.50 | 0.30124 | 46.2375 | 38.772 | 17.7667 |
| 29 | 1645.23 | 987.14 | 19.50 | 0.21875 | 46.3166 | 27.4469 | 19.0017 |
| 30 | 1699.67 | 956.066 | 19.50 | 0.26857 | 45.2226 | 32.5677 | 17.8242 |

| 20 | 1230.47 | 734.785 | 19.50 | 0.22288 | 25.7495 | 15.4863 | 10.5282 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 21 | 1560.02 | 780.012 | 19.50 | 0.33333 | 31.6378 | 31.6378 | 11.8642 |
| 22 | 1900.29 | 950.146 | 19.50 | 0.33333 | 46.9444 | 46.9444 | 17.6042 |
| 23 | 1697.84 | 914.22 | 19.50 | 0.29583 | 42.2392 | 34.481 | 16.2981 |
| 24 | 1767.05 | 951.486 | 19.50 | 0.29583 | 45.7529 | 37.3493 | 17.6538 |
| 25 | 1606.87 | 918.211 | 19.50 | 0.25758 | 41.3508 | 28.4287 | 16.4407 |
| 26 | 1905.95 | 952.976 | 19.50 | 0.33333 | 47.2245 | 47.2245 | 17.7092 |
| 27 | 1728.66 | 987.801 | 19.50 | 0.25758 | 47.8563 | 32.902 | 19.0271 |
| 28 | 1789.73 | 954.521 | 19.50 | 0.30124 | 46.2375 | 38.772 | 17.7667 |
| 29 | 1645.23 | 987.14 | 19.50 | 0.21875 | 46.3166 | 27.4469 | 19.0017 |
| 30 | 1699.67 | 956.066 | 19.50 | 0.26857 | 45.2226 | 32.5677 | 17.8242 |

| 31 | 1754.18 | 1052.51 | 19.50 | 0.21875 | 52.6541 | 31.2024 | 21.6017 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 32 | 1627.88 | 957.578 | 19.50 | 0.23545 | 44.1812 | 27.8342 | 17.8806 |
| 33 | 1863.39 | 986.501 | 19.50 | 0.30529 | 49.5411 | 42.4056 | 18.9771 |
| 34 | 1918.08 | 1078.92 | 19.50 | 0.26857 | 57.5912 | 41.4751 | 22.6992 |
| 35 | 1972.81 | 1109.71 | 19.50 | 0.26857 | 60.9249 | 43.8759 | 24.0132 |
| 36 | 2027.59 | 1140.52 | 19.50 | 0.26857 | 64.3552 | 46.3464 | 25.3652 |
| 37 | 2082.41 | 1171.35 | 19.50 | 0.26857 | 67.8822 | 48.8864 | 26.7554 |
| 38 | 2137.26 | 1202.21 | 19.50 | 0.26857 | 71.5058 | 51.4959 | 28.1836 |
| 39 | 2192.16 | 1233.09 | 19.50 | 0.26857 | 75.226 | 54.1751 | 29.6499 |
| 40 | 2247.08 | 1263.98 | 19.50 | 0.26857 | 79.0429 | 56.9239 | 31.1543 |

| 31 | 1754.18 | 1052.51 | 19.50 | 0.21875 | 52.6541 | 31.2024 | 21.6017 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 32 | 1627.88 | 957.578 | 19.50 | 0.23545 | 44.1812 | 27.8342 | 17.8806 |
| 33 | 1863.39 | 986.501 | 19.50 | 0.30529 | 49.5411 | 42.4056 | 18.9771 |
| 34 | 1918.08 | 1078.92 | 19.50 | 0.26857 | 57.5912 | 41.4751 | 22.6992 |
| 35 | 1972.81 | 1109.71 | 19.50 | 0.26857 | 60.9249 | 43.8759 | 24.0132 |
| 36 | 2027.59 | 1140.52 | 19.50 | 0.26857 | 64.3552 | 46.3464 | 25.3652 |
| 37 | 2082.41 | 1171.35 | 19.50 | 0.26857 | 67.8822 | 48.8864 | 26.7554 |
| 38 | 2137.26 | 1202.21 | 19.50 | 0.26857 | 71.5058 | 51.4959 | 28.1836 |
| 39 | 2192.16 | 1233.09 | 19.50 | 0.26857 | 75.226 | 54.1751 | 29.6499 |
| 40 | 2247.08 | 1263.98 | 19.50 | 0.26857 | 79.0429 | 56.9239 | 31.1543 |

| 41 | 2302.04 | 1294.9 | 19.50 | 0.26857 | 82.9564 | 59.7423 | 32.6968 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 42 | 2121.32 | 1116.48 | 19.50 | 0.30843 | 63.6092 | 55.34 | 24.3075 |
| 43 | 1973.48 | 1142.54 | 19.50 | 0.24792 | 63.5323 | 42.0048 | 25.4553 |
| 44 | 2018.51 | 1168.61 | 19.50 | 0.24792 | 66.4645 | 43.9435 | 26.6302 |
| 45 | 2063.56 | 1080.91 | 19.50 | 0.31094 | 59.7346 | 52.6586 | 22.7832 |
| 46 | 2108.62 | 1054.31 | 19.50 | 0.33333 | 57.8017 | 57.8017 | 21.6756 |
| 47 | 2153.7 | 1076.85 | 19.50 | 0.33333 | 60.2996 | 60.2996 | 22.6123 |
| 48 | 2418.68 | 1151.75 | 19.50 | 0.35337 | 70.0163 | 79.5852 | 25.8673 |
| 49 | 2243.91 | 1175.38 | 19.50 | 0.31094 | 70.6323 | 62.2654 | 26.9396 |
| 50 | 2289.03 | 1199.02 | 19.50 | 0.31094 | 73.5017 | 64.7949 | 28.034 |
| 51 | 2334.17 | 1222.66 | 19.50 | 0.31094 | 76.429 | 67.3754 | 29.1505 |

| 41 | 2302.04 | 1294.9 | 19.50 | 0.26857 | 82.9564 | 59.7423 | 32.6968 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 42 | 2121.32 | 1116.48 | 19.50 | 0.30843 | 63.6092 | 55.34 | 24.3075 |
| 43 | 1973.48 | 1142.54 | 19.50 | 0.24792 | 63.5323 | 42.0048 | 25.4553 |
| 44 | 2018.51 | 1168.61 | 19.50 | 0.24792 | 66.4645 | 43.9435 | 26.6302 |
| 45 | 2063.56 | 1080.91 | 19.50 | 0.31094 | 59.7346 | 52.6586 | 22.7832 |
| 46 | 2108.62 | 1054.31 | 19.50 | 0.33333 | 57.8017 | 57.8017 | 21.6756 |
| 47 | 2153.7 | 1076.85 | 19.50 | 0.33333 | 60.2996 | 60.2996 | 22.6123 |
| 48 | 2418.68 | 1151.75 | 19.50 | 0.35337 | 70.0163 | 79.5852 | 25.8673 |
| 49 | 2243.91 | 1175.38 | 19.50 | 0.31094 | 70.6323 | 62.2654 | 26.9396 |
| 50 | 2289.03 | 1199.02 | 19.50 | 0.31094 | 73.5017 | 64.7949 | 28.034 |
| 51 | 2334.17 | 1222.66 | 19.50 | 0.31094 | 76.429 | 67.3754 | 29.1505 |

As it is demonstrated in (figure-4) which is comparison between the vertical seismic profiles (VSP) of the bore hole WVT-1, which include the P-wave and the S –waves profiles, the lithology of the nearest borehole which is it BH126 and the SPT values of the same borehole. The WVT1 vertical seismic profiles show that the top 21.0 meters have clear variation in the velocities which could be related to the multi soil layers of different constituents and stiffness. From Depths 21.0 to 33.0 meters the VSP still showing variation because of the difference in soil constituents and they indicate more stiffness in the soil. While from depth 33.0 to 41.0 meters the VSP indicate one solid layer that shows increasing in the stiffness with depth. At depths of 41.0 and 42.0 there is clear drop in the seismic velocities which could be resulted from more clayey soil layer. Beyond the 42.0 meters depth the VSP shows a gradual increasing in the stiffness of the soil layer with the depth.

In figure-5 there is also a comparison  between the vertical seismic profiles of the bore hole WVT-2, which include the P-wave and S –waves profiles, the lithology of the nearest borehole which is it BH137 and the SPT values of the same borehole. The WVT2 vertical seismic profiles however, show almost the same behavior of the VSP of the borehole WVT1 but with differences in the depths ranges of the soil layers that were indicated by the seismic velocities. Also it can be noticed that at depth of 53.0-54.0 meters there is a strong increase in the seismic velocities which could reflect a very compacted sandy soil with very high stiffness.

It can be noticed in both (figure-4) and (figure -5) that there is a great agreement between the results of the VSP, the data of the lithology and the results of the Standard Penetration Test (SPT) of this area, which indicate the reality of the VSP data.

SPT Depth

Lithology of BH 126

(Figure-4) the VSP of borehole WVT1 on the right with the lithology and the SPT values of borehole 126

SPT Depth

Lithology of BH137

(Figure-5) the VSP of borehole WVT1 on the right with the lithology and the SPT values of borehole 137

Conclusions

There is very good relation between the seismic results and the lithology of the closes boreholes. However, it seems that the Vp and Vs curves show more details than the stratigraphic logs of these boreholes itself. There was convergence between the Vp and Vs curves and the results of the SPT test in the area. So the Downhole seismic velocity logging can be a good alternative method when the crosshole method is not possible for any reason.

Acknowledgment

Great thanks for Professor Dr. Basim R. Hijab for suggestion this research, supervision the field work and interpretation the seismic Data. Also thanks for Mr. Dhafir A. Al-Katib and Mr. Hamza M. Saeed for their great efforts in the field work.

References

Dobrin, M.B., (1976): Introduction to geophysical prospecting, (3rd edition). Mc Graw- Hill Inc. 630 p.

GEOVision, geophysical services, Downhole seismic velocity logging method, internal report.

GEOVision, geophysical services, Suspension P-S velocity logging method, internal report.

Standards, ASTM D7400 - 08 Standard Test Methods for Downhole Seismic Testing, Book of Standards Volume: 04.09.