Tradionally Phase Holdup Distribution Images of the Flow System by a Suitable Reconstruction Process

Abbas Ali Mahmood Karwi

Technical Institute of Babylon

Abstract

Dynamic three phase reaction and process systems are used widely in the chemical, petrochemical and biochemical industries. Dual Source Gamma ray Tomography (DSCT) has the potential for use as a non-invasive tool for determining the phases’ holdup distribution. Most of the dual source gamma ray and X-ray tomography methods reported in the literature use low energy gamma ray photons. These have poor penetration depths, thereby limiting their application to very small flow domains (~ 3in). However, since most flow domains are large, the use of higher energy gamma ray photons is inevitable. In this study, the 661 keV photon from Cs-137 and the 1332 keV photon from Co-60, have been explored for imaging phase holdup distribution in a gas-liquid-solid (GLS) system.

الخلاصة

الديناميكية التفاعلية للاطوار الثلاثة تستخدم بشكل واسع فى الصناعات الكيمياوية والبتروكيمياوية والبايوكيمياوية وان الكاشف المزدوج ثنائى النظائر المستخدمة لاشعة كاما يستخدم لايجاد التوزيع الطورى وان اكثر هذة الكواشف ذات طاقة فوتون واطئة للذا فان لها قدرة اختراق ضعيفة مما يجعل منها محدودة فى العمل بحيث لايتعدى قطر النموذج الاختبارى عن 3 انج ولزيادة القدرة التشخيصية يجب استخدام كواشف ذات طاقة عالية لذا تم استخدام نظائر السيزيوم-137 بطاقة فوتونية مساوية الى 661 كيلوالكترون فولت والكوبلت بطاقة 1332 كيلوالكترون فولت لتصوير التوزيع الطورى الثلاثى السائل والصلب والغاز.

Notation used

d(y)            Photon counts received by detector y

E                Mean of the given function

g(y : μ)       Mean value of photon counts received for a given y and μ

h(y|x)         Length of the segment of projection y in pixel x(cm)

I                 Number of photon counts generated by simulation

I (a||b)        I-divergence of quantities a and b

M(y|x)       Conditioned expected values of photons that enter pixel x along projection

n               Number of samples of counts data used to estimate the mean counts for each projection

N(y|x)        Conditioned expected values of photons that survive and leave pixel x along projection y

pX(y|x)             Probability of a complete data set x Index for pixel in image space

X(y|x)        Random number of photons entering a pixel x along projection y

y                Index for projection or source detector pair

ε(x)            Holdup fraction of any given phase

λ                Source intensity (counts)

μˆ (x)         Attenuation values estimated by algorithm for a given pixel x (cm−1)

μPhantom(x)  Attenuation value of a simulated phantom for which transmission data are generated (cm−1)

1.Introduction

Multiphase reaction and process systems are an integral part of a wide range of industrial processes associated with chemical and biochemical transformations and separations. The phases’ holdup distribution in such systems has a direct bearing on its performance. Hence, it is crucial to determine the effect of operating and design variables on the phases’ holdup distribution in such systems. Since most multiphase systems are opaque, a non-invasive experimental technique such as gamma ray tomography (Devanathan, 1991; Bhusarapu, 2005; Han, 2007; Al-Dahhan,  2009) is most desired for determining the phase holdup distribution. Single source gamma ray tomography, which uses gamma ray photons of a single energy from an isotope, has been used to determine the phase holdup distribution in two phase flow systems and in gas-liquid-solid (GLS) systems where the solid phase is stationary (Roy et al., 2002; Shehata, 2005). Some of the applications include determining the phase holdup distribution of liquid and gaseous phases in packed bed and monolith reactors (Al-Dahhan, 2009). However for imaging dynamic three phase systems, dual source gamma ray tomography is required. If the gamma photons of the two different energies used are from the same isotope the technique is called dual energy tomography. Low energy gamma emitting isotopes have been employed for determining phase holdup in small flow domains (~3 in.) that involve gas-oil-water systems. However, since they have a small penetration depth, they can not be used for applications that involve larger flow domains. Hence higher energy gamma ray photons have to be used for such applications. Gamma photons from Cs-137 (661keV) and Co-60 (1330 keV) isotopes are suitable for dual source tomography for three phase dynamic systems. The typical approach followed involves first reconstructing the attenuation profile or images based on the gamma ray transmission data of the GLS system (Varma, 2008; Vesavikar, 2006). This includes separate reconstruction from the transmission data of the two gamma ray photon energies. In the second step, post image reconstruction, the attenuation values of the individual phases for both the energies are used to determine the holdup fraction of each of the three phases in the GLS system. Since the reconstruction process in the first step involves processing data from a single energy at a time, we call this two step process the monoenergetic approach to dual source or dual energy tomography. The monoenergetic approach is the standard approach (Al-Dahhan, 2009,Bhusarapu, 2005; Boer, 2009) In this work, transmission data from both the energies was used for image reconstruction simultaneously. This approach is called polyenergetic. The polyenergetic model of the Alternating-Minimization (AM) algorithm proposed by (Al-Dahhan, 2009) has been applied to dual source gamma ray tomography. It is compared to the monoenergetic approach, as typically followed in the literature. The monoenergetic model of the AM algorithm was used, along with simulated gamma ray transmission data.

2.Alternating minimization algorithm [AM]

(O’Sullivan and Benac, 2007) formulated the maximum likelihood problem as a double minimization of an I-divergence to obtain a new image reconstruction algorithm called the Alternating Minimization (AM) algorithm. This iterative algorithm accounts for the stochastic nature of the gamma ray photons.   I-divergence, a concept introduced by (Csiszلr, 1991)  measures the inconsistency between two given functionsand, and is defined as:

----------------------------------------------------------------(1)

----------------------------------------------------------------(1)

The AM image reconstruction algorithm employs the I-divergence for image reconstruction. It is based on a statistical model for the measured gamma ray counts data, Beer Lambert’s law, and a model for the known point spread function. The reconstruction problem is formulated as an optimization (maximum likelihood) problem in statistical estimation theory. This algorithm is described in brief here for continuity, further details of the mathematical proof of the algorithm are available elsewhere (O'Sullivan and Benac 2007).

3. Polyenergetic Alternating Minimization (AM) algorithm

The incident photo spectrum of the photons form an x ray source is inherently polyenergetic in nature. Many image reconstruction algorithms related to x ray tomography for medical imaging have been developed that model the polyenergetic nature of the incident x ray photon spectra (O'Sullivan and Benac 2007), there by capturing the physics of the transmission process better. The prime motivation for a model that accounts for the energy of the photons is to reduce beam hardening artifacts that occur in the reconstructed images when a monoenergetic (ME) model is used for spectrum that is polyenergetic (PE) in nature. This artifact appears especially if the domain has high attenuating materials like bone or metallic implants that are typical in medical imaging. The gamma spectrum consisting of either single or multiple photo peaks ,on the other hand has a discrete spectrum. This allows for the use of energy discrimination electronic hardware associated with the data acquisition system to acquire photon counts data with a specific energy, even if poor energy resolution detectors are used. This also helps to avoid counting of the Compton scatter counts especially if a single discrete gamma photo peak is emitted by the source as in the case of Cs137 . Hence ME models are typically used to model the transmission of γ photons tomography and beam hardening artifacts are rare due to the high energy of the γ photons. In this section the polyenergetic version of the alternating minimization (PE-AM) algorithm as proposed by (O'Sullivan and Benac 2007) is applied to the dual energy γ computed tomography problem .The PE-AM algorithm could be applied such that it accounts for the energy of the γ photons and processes the counts data from both the energies of the gamma ray photons . If, which represents the counts received by the detector, is modelled as a Poisson random variable with mean defined by,

------------------(2)

--------------------------------------------------------(3)

--------------------------(4)

---------------(5)

-------------------------------------------------------------------(6)

------------------------------------------------------------------------(7)

---------------------------------------------(8)

---------------------------      -----------------------------------(9)

----------------------------(10)

--------------------------------(11)

2.2Monoenergetic Alternating Minimization (AM) algorithm

-------------------------------------------------------------------------------------------------------(12)

--------------------------------------------------------------------------------------------------------------(13)

---------------------------------------------------------------------------------------------------------------(14)

------------------------------------------------------------------(15)

---------------------------------------------------------------(16)

-------------------------------------------------------------------------------------(17)

-------------------------------------------------------------------------------(18)

---------------------------(19)

---------------------------(20)

---------------------------------------------------------------------(21)

-

---------------------------(22)

---------------------------(22)

3. Details of the pebble bed reactor and data simulation

Circular domain of 12 in. diameter consisting of air (gas), and lead glass (solid)  with diameters equal to 0.5, 1, 2 in dispersed uniformly across the domain. This is comparable to a hypothetical dynamic GS flow system where the time averaged holdup distribution of the individual phases is uniform across the domain. The gamma ray transmission data for both the radioactive isotopes was simulated using Schaffer’s algorithm. This algorithm generates Poisson random numbers with a given mean value. The nonlinear model for transmission of photons for each projection was used as the mean value for generating the Poisson random numbers (Bazant, 2004; Hassan & Dominguez-Ontiveros, 2008; Boer, 2009) , the photon counts received by the detectors. In pressurized pebble reactor, Helium coolant flows under a high Reynolds number flow conditions through the reactor core and cools the heated, randomly and closely distributed pebbles. Physically, these pebbles in the core are in contact with each other. Hence, the interaction between the flowing gas phase and the heat generating pebbles makes the flow and heat transport characteristics complicated (Mueller, 1992; Lee, 2009). On the other hand, mixing and the dispersion of the gas phase directly affect the amount of heat removal from the reactor. The local high temperature gradients and hot spots should be avoided in the core of PBR via proper design and safe operation. Also, the efficiency of the reactor is dependent upon the distribution of flowing gas phase throughout the bed. Hence, an experimental measurement of the gas distribution in the PBR is practically useful in design and operation of these reactors. There is an attempt to measure the local velocity field with particle tracking velocimetry (PTV) technique  in a small sized ( 3cm x 3cm x 35 cm) packed bed using refractive index matching liquid. In another  studies (Rammohan, 2002; Mueller, 2005; Ryeroft el al., 2006), flow field measurements are carried out in a two-dimensional wind tunnel by particle image velocity (PIV) technique in the very narrow flow channel between the pebbles.  This study also involved small sized pebble bed test section (170mm x 170mm x 505 mm).  The advanced gas dynamics tracer technique is being applied to PBR gas dynamics study at Missouri S&T to initiate for the first time gas dynamics and dispersion study in the pebble beds.

4. Selected experiments and data analysis:

Experiments used  air  as a gas phase in the pebble bed while (helium) is used as a tracer. The flow rate of air is kept at 0.02 m3/s which is equivalent to a superficial gas velocity (Ug) of         20 m/s based on 30 cm internal diameter of pebble bed. The procedure used to process the obtained data is discussed below as shown as shown in Table(1), Fig(1).

Table 1. Set of experimental measurements for the gaseous tracer technique

Table 1. Set of experimental measurements for the gaseous tracer technique

I1, I2: Injection ports; S1, S2, S3: sampling ports

I1, I2: Injection ports; S1, S2, S3: sampling ports

| Measurement | Tracer injection | Sampling location | Dispersion zones measured |
| --- | --- | --- | --- |
| C(i) | I1 | S1 | sampling/analytical system from S1 |
| C(ii) | I1 | S2 | plenum zone + sampling/analytical from S2 |
| C(iii) | I2 | S3 | sampling/analytical system from S3 |
| C(iv) | I1 | S3 | plenum zone + reactor zone +sampling/analytical system from S3 |

d

d

c

c

a,b

a,b

Figure 1. Diagram of the convolution and model fits of the response curves

Figure 1. Diagram of the convolution and model fits of the response curves

Figure 2. Schematic diagram of the advanced gas dynamics experimental set-up

Figure 2. Schematic diagram of the advanced gas dynamics experimental set-up

5. Mass balance checking

Mass balance assessment needs to be carried out in order to ensure that the injected amount of tracer is going in and leaving the system. Ideally, certain amount of gas tracer (helium gas) should be injected suddenly into the pebble bed in a shortest time (less than 1 sec) as possible to achieve proper impulse input. At the same time, injected helium amount should be sufficient to get detected properly. The appropriate time interval of injection  is found to be of 0.5 sec by trial and error. This time of injection has been used for all tracer injections. Based on total mass balance, the quantity of the injected tracer has been found to be 4.5g. This is equivalent of mass flow rate of 9 g/sec or volumetric flow rate of 50 cm3/sec of helium.

6. Normalization of the raw data

This is an important step in which the measured signals for each compartment are normalized by the maximum and minimum values of the output tracer concentrations. This is being done for qualitative comparison of different compartment signals and will also be used in the next steps. Figure 5 shows gas tracer concentration results obtained for different sampling positions corresponding to the Table 1 .

Figure 3.  RTD responses of the gas tracer obtained for different sampling positions Ug=60 cm/s, time interval of

injection = 0.5 sec , d=12in , h=1ft

Figure 3.  RTD responses of the gas tracer obtained for different sampling positions Ug=60 cm/s, time interval of

injection = 0.5 sec , d=12in , h=1ft

It seems that the C(i) measurement is less dispersed as compared to the C(ii) measurement. This confirms the occurrence of low dispersion in the sampling lines as compared to the plenum dispersion. This is necessary from proper data analysis point of view and to characterize properly the dispersion occurring in the plenum. The same trend is observed for the C(iii) measurement, due to the identical design of sampling lines. The aim is to decrease the dispersion occurring in the sampling system, in order to properly estimate the dispersion occurring in the plenum and the pebble bed itself. Based on the theoretical analysis of the moments for the RTD responses, the moments of the compartments of the set-up are additive. This allows estimating the moments of the pebble bed section without pre-assuming the type of the model as per Figure 1.

7. Validation of CSTR model assumption for the inlet plenum/distributor

The gas phase mixing occurring in the plenum and distributor is assumed to be of a continuous stirred tank reactor (CSTR) type while processing the data for the convolution of the RTD signals .

This assumption needs to be validated first in order to use it as an input to the suggested bed model which in this case is an axial dispersion model (ADM). The plenum output in a dimensionless form (Cin) is defined as (C/Cinj) and is given by Equation 1.

-----------------------------------------------------------------------------------(1)

-----------------------------------------------------------------------------------(1)

Where; τ0 = the residence time for the CSTR model to be estimated for the plenum/distributor zone by    curve fitting experimental data (volume/volumetric flow rate, RTD response curve).

t = time at any instant

In this step, the first two measurements signals i.e. C(i) and C(ii)) are used. First, C(i) is used as an input to CSTR model (equation 1), and then calculated Cin is used to get Cin* which is the convoluted plenum CSTR predictions (Equation 3) .

------------------------------------------------------------------(2)

------------------------------------------------------------------(2)

This Cin* is compared with the C(ii) measurement which is the experimentally obtained response of the plenum plus distributor, and the top sampling system together . Then optimization of τ0 is carried out to match the convoluted plenum CSTR predictions with the experimental results. This is done by minimizing an error (averaged squared type) defined as follows:

------------------------------------------------------------------(3)

------------------------------------------------------------------(3)

A good match is observed between C(ii) measurement and the predicted Cin* (Figure 7) which indicates that the gas mixing occurring in the plenum and distributor can be modeled as a CSTR. The averaged squared error calculated using Equation 4 is found to be 6.328E-4. The Cin calculated from the plenum CSTR model with a fitted τ0 (τ0 = 0.53 sec) is used as an input tracer profile to the reactor model instead of an idealized delta function input. This is necessary in order to incorporate back-mixing occurring in the plenum and distributor before the pebble bed.

Figure 4. Dynamic gas tracer concentration results at the plenum distributor with CSTR model fit (Ug=60 cm/s).

Figure 4. Dynamic gas tracer concentration results at the plenum distributor with CSTR model fit (Ug=60 cm/s).

8.Mathematical representation of the gas phase dispersion occurring in the pebble bed by axial dispersion model

The one-dimensional axial dispersion model (ADM) is used initially to represent mathematically the dispersion of the gas phase occurring in the pebble bed zone. This approach is first assessed experimentally and then used to estimate the axial dispersion coefficient (Dg). The C(iii) measurement is used as an input to convolute the reactor and plenum model predictions. Then, the Cin obtained from (Equation 2) (CSTR model of the plenum) is used as an input tracer profile to the suggested reactor model. This yields an output profile (Cout) for the pebble bed, which is then convoluted by C(iii) (Levenspiel, 1999) as below:

------------------------------------------------------------------(4)

------------------------------------------------------------------(4)

The convoluted bed model predictions (Cout*) then compared with the response of the whole system which is being obtained by the C(iv) measurement. Finally, optimization of an axial dispersion coefficient (Dg) is carried out to match the convoluted reactor model (i.e. ADM) predictions with experimental results as shown in the Figure 8. This is performed by minimizing the error, which is defined as the average of difference between squares of Cout* and C(iv) (Equation 5).

Figure 5. Dynamic gas tracer concentration at the outlet with ADM fit (Ug=60 cm/s)

Figure 5. Dynamic gas tracer concentration at the outlet with ADM fit (Ug=60 cm/s)

The axial dispersion coefficient (Dg) is found to be 2.93 m2/s. This value indicates a deviation (which is relatively not very large) from the idealized plug flow in a tubular packed bed.  The averaged squared error calculated by equation 6 is 1.28E-3. A good match is observed between Cout* and C(iv) (Figure 6) which indicates that dispersion occurring in the pebble bed can be represented mathematically by one dimensional ADM model at the studied conditions. In future, different mathematical strategies based on CSTR tanks-in-series model and moments analysis will be used to extract the pebble bed response without assuming any predefined dispersion model for the reactor. The calculations of Dg are repeated using a delta function as an input to ADM instead of Cin. This is to check the effect of extra dispersion occurring in the plenum on values of Dg. This predicts higher Dg values and suggests that ignoring the extra dispersion occurring in the plenum introduces significant error in the prediction of Dg. This has been already reported in the study carried out on slurry bubble columns (Lu Han, 2007).

9.Initiation of the quantification of the gas phase mixing and dispersion based on central moment analysis

Moments analyses are among the methods used to quantitatively analyze the dispersion of residence time distribution (RTD) curves obtained by tracer technique.  Table 2 summarizes the definition of the four central moments and the relationships used to estimate them in terms of tracer concentration C(t) and age distribution function E(t) curve for impulse tracer injection. The moments are follows:

1- The zero moment represents the area under the curve on the time response graph of tracer concentration. This moment is useful for mass balance assessment that needs to be carried out in order to ensure that the injected amount of tracer leaves the system.

2- The first moment of the residence time distribution represents the mean age of the tracer in the pebble bed, if there is no considerable diffusion transport across inlet and outlet boundaries.

3- The second moment about the mean of residence time is a measure of the dispersion of the distribution and is called the square of the standard deviation (σ2) or the variance.  The magnitude of this moment is an indication of the spread of the distribution around the mean. Greater the value of this moment, wider will be the spread of distribution.

4-The third central moment of the distribution known as Skewness will provide the information about the relative weight that the various fractions of feed will have on the total dispersion. The magnitude of this moment measures the extent that a distribution is skewed in one direction or another in reference to the mean.

Estimating theses moments allows qualifying the dispersion in the system without assuming any predefined model for the pebble bed.  It has been known and proven that the moment quantities are additives for system in series. Therefore, using our advanced tracer technique, where we can have the response of all its components, we will be able to extract the moments for the pebble bed alone. This will further allow analyzing the dispersion encountered in pebble beds. In previous analyses, we quantify the tracer response of the bed using ADM. In this case we can process the ADM response curve to estimate its moments, where these moments of the bed will be compared with the moments obtained from the raw tracer response data. Such comparison will further give insight on whether ADM can be used to estimate the dispersion in the pebble bed.

Table 2.  Expressions of the moments for the impulse tracer response in pebble bed

| Central moments | Physical meaning | Relationship in terms of outflow concentration, C(t) | Relationship in terms of RTD function, E(t) |
| --- | --- | --- | --- |
| Zero moment | area under the curve |  |  |
| First moment | mean residence time |  |  |
| Second moment | variance |  |  |
| Third moment | Skewness |  |  |

10-Experimental investigation of pebble bed structure in terms of solids and voids distribution using gamma ray densitometry and gamma ray computed tomography (CT)

Tomography is a powerful visualization technique which produces time averaged cross-sectional images of multiphase domain in a non-invasive manner. A dual energy, dual source γ-ray tomography (DE-DSCT) system developed by Dr. Muthanna-Al-Dahhan and his group at Washington University and collaborators from Oak Ridge  National Laboratory as a part of previous DOE grant had been transferred to Missouri S&T. Dr. Rajneesh Verma, who was part of the developing team and work was part of his PhD research under Dr. Muthanna-Al-Dahhan’s supervision, visited our lab and provided training sessions on the mechanical and electronic components and tuning of the system which helped in faster learning about system and its operation. The electronics of DE-DSCT system is tested extensively during the current quarter. The main activities include continuity testing of each channel, Multichannel analyzer (MCA) mode based peak identification, adjustment of detector and pulse processing module gains to bring peak within operating range. Each source is positioned at the centre of the respective detector array plate using laser alignment. The reference pointer and scale is installed between both detector array plates and circular plate and also between circular plate and fixed plate. The relative position of the source with respect to detector array plate is marked as a reference position. This is essential in order to check if there is any drift in relative position after performing long lasting experiments.

This DE-DSCT uses two separate γ-ray sources, Cs-137 and Co-60 (emitting γ photons of different energies), and is capable of imaging 3-phase flow encountered in a wide variety of multiphase systems. During the current quarter, DE-DSCT radioactive sources are transferred from Washington University and installed on the set-up.  All the radiation safety measures have been established and implemented in our lab (Fulton Hall G-2).Gas-liquid phantom based experiments has been initiated. This will give an opportunity to validate the system data acquisition programs and data processing algorithms before applying them on Pebble bed reactor study. DE-DSCT system will be used for imaging cross-sectional solids and voids distribution in the Pebble bed reactor experimental set-up developed at Missouri S&T. The determination of porosity distributions at various heights and its variation with pebble diameter and exit flow rate in the bed is a crucial knowledge. Such information complements the knowledge that has been obtained from the gas dynamics tracer experiments and the knowledge that will be obtained from the radioactive particle tracking (RPT) technique.

Figure 6.  DE-DSCT  setup (a) Entire set-up with sources and (b) pebblebed reactor

Figure 6.  DE-DSCT  setup (a) Entire set-up with sources and (b) pebblebed reactor

Figure 7.  DE-DSCT  setup (a) Entire set-up with sources and (b) pebblebed reactor

Figure 7.  DE-DSCT  setup (a) Entire set-up with sources and (b) pebblebed reactor

11. Results and discussion

a- Senogram of pebblebed reactor-12in diameter-1ft height-1 in Marbles

a- Senogram of pebblebed reactor-12in diameter-1ft height-1 in Marbles

b- Senogram of pebblebed reactor-12in diameter-1ft height-0.5 in Marbles

b- Senogram of pebblebed reactor-12in diameter-1ft height-0.5 in Marbles

c- Senogram of pebblebed reactor-12in diameter-1ft height-2 in Marbles

c- Senogram of pebblebed reactor-12in diameter-1ft height-2 in Marbles

Figure 8.  Images of  senogram  for  pebblebed reactor with 1ft heigt and 12in diameter  obtained with the AM algorithm after 500  iterations with hz = 5,  a- Marbles  diam=1in ,b- Marb diam=0.5 in, c- Marbles diam=2in.

Figure 8.  Images of  senogram  for  pebblebed reactor with 1ft heigt and 12in diameter  obtained with the AM algorithm after 500  iterations with hz = 5,  a- Marbles  diam=1in ,b- Marb diam=0.5 in, c- Marbles diam=2in.

c- Transmission of pebblebed reactor-12in diameter-1ft height-2 in Marbles

b- Transmission of pebblebed reactor-12in diameter-1ft height-0.5 in Marbles

a- Transmission of pebblebed reactor-12in diameter-1ft height-1 in Marbles

Var=0.19297; STD=0.439

Var=0.195359; STD=0.4419

Var=0.199173; STD=0.446286

Figure 9.  Standard deviation  & variance of sonogram  for results obtained with AM algorithm , a- Marblesdiam=1in

b- Marbles diam=0.5in , c- Marbles diam=2in

c- Transmission of pebblebed reactor-12in diameter-1ft height-2 in Marbles

b- Transmission of pebblebed reactor-12in diameter-1ft height-0.5 in Marbles

a- Transmission of pebblebed reactor-12in diameter-1ft height-1 in Marbles

Var=0.19297; STD=0.439

Var=0.195359; STD=0.4419

Var=0.199173; STD=0.446286

Figure 9.  Standard deviation  & variance of sonogram  for results obtained with AM algorithm , a- Marblesdiam=1in

b- Marbles diam=0.5in , c- Marbles diam=2in

A test reactor with a resolution of 80x80 pixels was used in this study. The reactor  represents a circular domain of 12 in. diameter consisting of marbles with diameters 0.5, 1, 0.5 in  dispersed uniformly across the domain. This is comparable to a hypothetical dynamic GS flow system where the time averaged holdup distribution of the individual phases is uniform across the domain. The gamma ray transmission data for both the radioactive isotopes was simulated using Schaffer’s algorithm. This algorithm generates Poisson random numbers with a given mean value. The nonlinear model for transmission of photons for each projection (line across the domain),  was used as the mean value for generating the Poisson random numbers. The random numbers were used as the representation the photon counts received by the detectors. A gamma ray scanner with a fan beam arrangement of source and detectors was considered. Data based on 197 source positions and 21 projection for each source position were considered. The values of were calculated based on an 80x80 pixel domain in this scanner. The approximate photon counts that would be received with a 235 mCi Cs 137 isotope and 50 mCi Co 60  isotope for the same scanner geometry were chosen as the incident photon counts . The counts data generated for both the energies (661 keV fromCs137 and 1332 keV from Co60) were processed by the polyenergetic and the monoenergetic models of the AM algorithm for 500 iterations. A quantitative analysis of the images is possible only when the senogram values of all pixels in a given part of the image are analyzed for its standard deviation. Standard deviation indicates the level of noise in the image. If the standard deviation of the pixels is high, it means that the image is noisy and a lot of freckles or grains can be seen. The most desirable situation is the one where both the standard deviation and the error are nil. When the standard deviation is small and the error is high, then there is a bias in the image.

The results indicate that for the same transmission data, the polyenergetic approach gives far superior results to the monoenergetic approach. The monoenergetic approach is sensitive because of the attenuation of the materials at the gamma ray photon energies chosen. Hence, a very small error in estimating the attenuation values which is unavoidable due to the stochastic nature of gamma ray photons . The AM algorithm is known to give more accurate results [19]  However this improved accuracy is still not sufficient to solve the dual source tomography problem using Cs137 and Co60 sources. The polyenergetic approach, on the other hand is far more promising for solving this problem. In this way, the post image reconstruction approach is avoided. The polyenergetic approach based on the AM algorithm shows promising potential for determining the phase holdup distribution in three phase dynamic systems using dual source gamma ray tomography (DSCT).

12. Discussion

The AM algorithm was successfully implemented for the case of single energy gamma ray tomography to determine phase holdup images for two phase systems for pebblebed reactor with different marbles diameters. The performance of the algorithm was compared by putting the effect of some critical parameters, such as the noise level and the number of iterations used to reconstruct the image. A systematic quantitative analysis of the senogram images generated using the AM algorithm was carried out for the three cases of the reactor. Applications that involve the use of high attenuation material the AM algorithm is more stable and produces senogram images that have a greater degree of accuracy and lower levels of noise. This is true for both parts of the domain that have the high attenuation material (metals) and parts that do not have it, like the surrounding areas. Hence, the AM algorithm is a better choice for image reconstruction for determining the holdup distribution images in multiphase systems involving two-phase flow.

13. References

Al-Dahhan M., 2009, Radioisotopes applications in industry: an overview, Atoms for Peace: international Journal, Vol. 2 (4), pp. 324 - 337.

A., Bazant M., 2004, Pebble flow experiments for pebble bed reactors, 2nd International Topical Meeting on High Temperature Reactor Technology, Beijing, China, September 22-24.

Bhusarapu S., 2005, Solids flow mapping in gas solid risers, DSc thesis, Washington University, St. Louis.

Boer B., 2009, Optimized core design and fuel management of a pebble-bed type nuclear reactor, Ph.D. thesis, Delft University of Technology, Delft, Netherlands.

Devanathan, N., 1991, Investigation of Liquid Hydrodynamics in Bubble Columns via Computer Automated Radioactive Particle Tracking (CARPT), D. Sc. Thesis, Washington University, St. Louis, Missouri.

Hassan Y., Dominguez-Ontiveros, E. 2008 “Flow visualization in a pebble bed reactor experiment using PIV and refractive index matching techniques” Nuclear Engineering and Design Vol. 238 , Pp. 3080-3085.

Han L., “Hydrodynamics, back-mixing, and mass transfer in a slurry bubble column reactor for Fischer-Tropsch alternative fuels” PhD thesis, Washington University in St. Louis  ,2007, Kadak

Lee, J. and  Lee, S. 2009, Flow Visualization in the scaled up pebble bed of high temperature gas-cooled reactor using particle image velocimetry method” Journal of Engineering for Gas Turbines and Power,  Vol. 131 pp. 064502/1-4.

Mueller G., 1992, Radial void fraction distributions in randomly packed fixed beds of uniformly sized spheres in cylindrical containers, Powder technology, 72, pp.269-275.

Mueller G., 2005, Numerically packing spheres in cylinders, Powder technology, 159, pp.105-110.

OSULLIVAN J.A., and BENAC J., 2007, Alternating Minimization Algorithms for Transmission,Tomography Medical  Imaging, IEEE Transactions on  26, 3, 283-297.

Rammohan A., 2002, Characterization of single and multiphase flows in stirred tank reactors, D.Sc. Thesis, Washington University, Saint Louis, Missouri.

Roy S., Larachi F., Al-Dahhan M.H., Duduković M.P., 2002, Optimal design of radioactive particle tracking experiments for flow mapping in opaque multiphase reactors, Applied Radiation and Isotopes, 56, pp. 485–503.

Rycroft C., Grest G., Landry J., and Bazant M., 2006, Analysis of granular flow in a pebble-bed nuclear reactor, Phys. Rev. E., 74, 021306.

R.Varma,J.A.OSullivan and M.H.Al-Dahhan,, Application of Alternating-Minimization (AM) in dual source Gamma ray computer tomography for Imaging Three Phase systems

Shehata A., 2005, A New Method for Radioactive Particle Tracking, Ph.D. Thesis, North Carolina State University, Raleigh, North Carolina.

Shehata A., 2005, A New Method for Radioactive Particle Tracking, Ph.D. Thesis, North Carolina State University, Raleigh, North Carolina.

Varma R., 2008, Characterization of anaerobic bioreactors for bio-energy generation using a novel tomography technique, PhD thesis, Washington University, St. Louis.

Vesavikar M., 2006, Understanding hydrodynamics and performance of anaerobic digesters, DSc thesis, Washington University, St. Louis.