Ch2(2)

slowly. The instantaneous velocity v of the car indicates how fast the car moves and the direction of the motion at each instant of time. The magnitude of the instantaneous velocity is called the instantaneous speed, and it is the number (with units) indicated by the speedometer.

The instantaneous velocity at any point during a trip can be obtained by measuring the time interval Δt for the car to travel a very small displacement Δ x. We can then compute the average velocity over this interval. If the time Δt is small enough, the instantaneous velocity does not change much during the measurement. Then, the instantaneous velocity v at the point of interest is approximately equal to (~) the average velocity computed over the interval, or v ~ vΔx/Δt (for sufﬁciently small t). In fact, in the limit that t becomes inﬁnitesimally small, the instantaneous velocity and the average velocity become equal, so that

2.3 Acceleration

The velocity of a moving object may change in a number of ways. For example, it may increase, as it does when the driver of a car steps on the gas pedal to pass the car ahead. Or it may decrease, as it does when the driver applies the brakes to stop at a red light. In either case, the change in velocity may occur over a short or a long time interval.

To describe how the velocity of an object changes during a given time interval, we now introduce the new idea of acceleration; this idea depends on two concepts that we have previously encountered, velocity and time. Speciﬁcally, the notion of acceleration emerges when the change in the velocity is combined with the time during which the change occurs.

The meaning of average acceleration can be illustrated by considering a plane dur-

Figure 2.6 (a) To slow down, a drag racer deploys a parachute and applies the brakes. (b) The velocity of the car is decreasing, giving rise to an average acceleration a¯ that points opposite to the velocity. (© Geoff Stunkard)